STD Commenter Information (For Individual Commenters)

Name Robert Blohm Organization Blackout Supplement Industry Segment # 8 Telephone 609 585 5451 E-mail rb112@columbia.edu

| STD Commenter Information (For Groups Submitting Group Comments) |
| --- |
| Name of Group: | Group Chair: Chair Phone: Chair Email: |
| List of Group Participants that Support These Comments: |
| Name | Company | Industry Segment # |

### Comments on Introduction to the Balance Resources and Demand Standard

- This standard introduced a set of limits for the RA to use in controlling frequency and a set of limits for monitoring the BA’s ACE.  Do you agree with the principle of using these limits as an aid in monitoring and controlling interconnection frequency?

Relay Limits

Agree with using the limits in this standard

Disagree with using the limits in this standard

Comments about using any of these limits in this standard

I mentioned this possible issue in The New York Times' first article (August 16th) covering the Blackout http://www.nytimes.com/2003/08/16/nyregion/16BLAC.html

High Frequency Relay LIMITS too high?  should they be based exclusively on damage to the piece of property?  could they have limited the blackout if set much tighter?  The policy of setting the high frequency relay limits exclusively on the basis of damage to the piece of property should be reconsidered in light of the 2003 Blackout and the fact that, unlike 1965 and 1977, the Blackout was characterized by over-frequency on the Interconnection.

This is due to the fact of the deregulated wholesale market since that time and the large individual control area imbalances that have existed since then in virtue of interregional trade/flows.  While islanding might have had little effect on the frequency of the remainder of the Interconnection during the previous Blackouts, this time it had the effect of ever higher over-frequency on the rest of the interconnection as transmission-protection relays tripped and net loads were islanded.  Current high-frequency relay limits of 62 Hz, based exclusively on damage to a piece of property, were too high to be tripped by the ever higher over-frequency of the remainder of the Interconnection, peaking at 60.25 Hz during the Blackout.  In this circumstance it might have been better for generators to have tripped to reduce both frequency and transmission loading rather than for transmission to have tripped to create an ever larger imbalance over an ever smaller transmission grid.

Consider the impact of islanding on Interconnection frequency in setting the high frequency relay limits?  Accordingly, in the current reality of high interconnection loadings in an ever growing interregional wholesale market, the effect of transmission curtailment, and of islanding, on frequency, should be considered as a possible factor to be included in the determination of the high-frequency relay limits, in recognition of the much higher level today of interconnected regional imbalances on the grid.  At the time of the 2003 Blackout high natural gas prices made power from Midwest coal-fired plants ever attractive to the Northeast.  Consideration would also have to be given to the location of the generation being tripped, such that it is generally on the supply side of the remaining flow on the interconnection, rather than on the demand side where tripping generation might only make the problem worse.  Dynamical consideration could be given to whether and how to change the location of the limiting high-frequency relays with big changes in flow pattern.

### Procedures for Developing Interconnection Frequency Limits, BAALs, and Frequency Bias

- Do you agree with the method of calculating these limits as described in the Procedure for Determining Interconnection Frequency Limits?

Relay Limits

Agree with the calculations for these limits

Disagree with the calculations for these limits

Comments about the calculations for these limits See comments to question 2

# Text boxes

Key to Industry Segment #’s:

1 – Trans. Owners

2 – RTO’s, ISO’s, RRC’s

3 – LSE’s

4 – TDU’s

5 - Generators

6 - Brokers, Aggregators, and Marketers

7 - Large Electricity End Users

8 - Small Electricity Users

9 - Federal, State, and Provincial Regulatory or other Govt. Entities